## Slide 1: Distributed Temperature Sensing (DTS) Overview
For PRODML v2.0

## Slide 2: Overview
This presentation deck includes slides for the set of objects for distributed temperature sensing (DTS). For more information, see the PRODML Technical Usage Guide, which is included in the zip file when you download PRODML from the Energistics website.

## Slide 3: DTS Introduction
Temperature measurement spatially distributed over thousands of points
Used in hundreds of facilities for, e.g.:
  real-time surveillance,
  status of gas lifted or steam wells,
  casing /tubing integrity,
  leak detection on pipelines
Use is growing and new fiber measurements are emerging

## Slide 4: Goals for PRODML DTS Project
Support requirements sufficient for industry-wide adoption.
  Data transmission, storage, and interfaces
  Fiber Asset Management
  Metadata
Provide PRODML schema & guidelines so vendor software can be interchangeable, allowing mix-and-match hardware and software
Create compelling standard that attracts OCs and vendors
...promoting products that plug into multiple vendors hardware for data acquisition and integrate out of the box with consumer products on the front-end.

## Slide 5: DTS Challenges
Data is traces (like logs) not point values
  ~ 1MB per trace per ~ minute per well
Configuration and condition of fiber needs to be known and managed
  Complex configurations becoming common
  Condition, faults etc. change over time
No standard interface for whole data transfer (earlier PRODML partial coverage and not fully standardized)

## Slide 6: Typical DTS System and challenges
Inventory Mgmt.
Field
Office Domain
DTS Repository
Historian &
Completion Data
PRODML V1 or other
Product Scope
Surveillance &
Analysis Tools
Wells
Pipelines
Heaters
Leak Detection…
DTS
Fiber
reliability problems
Proprietary
Proprietary and largely manual
Not related hence data not mapped to assets
DTS
Fiber
Config changes over time
Instrument
Box
Notes: Transport App: It’s the UPS for ASP.
  Robust and Reliable mechanism for sending data over to the office domain.
  Future Proof: Supports any type of advanced sensing data, not only DTS. (File based).
  Based on Shell Global Standards: No need for step-outs.
  Based on Industry Standards: Vendors can easily make use of the transport mechanism or its infrastructure (i.e. Schlumberger)
Traffic Light Web App: It’s the CNN for ASP
  Provide complete transparency on the status of the ASP world. Have confidence that ASP data is being generated and managed properly.
  Quality tagging of all data received. Early detection of problems down the line. Have confidence that ASP data is good and will be useful.
  Get notified when something goes wrong. Don’t find out when it’s too late.
Preview/Selection Site: It’s the Music Store for ASP
  Browse all the ASP related files that have been received in the office domain. No more digging around endless folders in network shares.
  Preview their contents before you download.
  Compare ASP data against PI readings to help you select the date range of your interest. No more manual filtering based on guesses.
  Compare ASP data against Well Completion data. Quickly determine the level of calibration that may be needed before attempting any time-consuming work.

## Slide 7: PRODML DTS Enhancements
Provide Standard interface for acquiring data from Instrument box of multiple vendors
Provide standard transport to move data across varying infrastructures and security zones.
Provide storage that retains current and historical information on fiber assets, and measurements/quality, calibration, and actions taken on/from these assets.
Provide a standard interface to allow visualization, analytics, and other consumers to access out of the box.

## Slide 8: Typical DTS System Exploiting PRODML
Transport App
Inventory Mgmt.
Portal
Field
Office Domain
DTS Repository
Historian &
Completion Data
View and Manage DTS related Assets
PRODML
PRODML
PRODML
Product Scope
Surveillance &
Analysis Tools
Wells
Pipelines
Heaters
Leak Detection…
DTS
Fiber
PRODML-enabled transport app resolves reliability problems
PRODML
DTS
Fiber
Config changes over time
PRODML
Instrument
Box
Notes: Transport App: It’s the UPS for ASP.
  Robust and Reliable mechanism for sending data over to the office domain.
  Future Proof: Supports any type of advanced sensing data, not only DTS. (File based).
  Based on Shell Global Standards: No need for step-outs.
  Based on Industry Standards: Vendors can easily make use of the transport mechanism or its infrastructure (i.e. Schlumberger)
Traffic Light Web App: It’s the CNN for ASP
  Provide complete transparency on the status of the ASP world. Have confidence that ASP data is being generated and managed properly.
  Quality tagging of all data received. Early detection of problems down the line. Have confidence that ASP data is good and will be useful.
  Get notified when something goes wrong. Don’t find out when it’s too late.
Preview/Selection Site: It’s the Music Store for ASP
  Browse all the ASP related files that have been received in the office domain. No more digging around endless folders in network shares.
  Preview their contents before you download.
  Compare ASP data against PI readings to help you select the date range of your interest. No more manual filtering based on guesses.
  Compare ASP data against Well Completion data. Quickly determine the level of calibration that may be needed before attempting any time-consuming work.

## Slide 9: Use Cases and Key Concepts

## Slide 10: Principle Use Cases
Configuration of & changes in fiber assets
  Optical path comprising: fiber segments, connectors, splices, conveyance, anomalies…
  Instrument box + path combinations: generate data
  Calibrations and condition monitoring
For an installed DTS system, transfer trace data from field to office
Transfer temperature data mapped from trace to actual facilities (wells, pipes, etc.)

## Slide 11: Top Level Data Objects
Optical Path
(series of fiber segments & components)
Instrument Box
(surface “Light Box” instrument)
Installed System
(path + box which makes measurements)
Measurement Set
(Measured Trace of raw data plus Log of temperature mapped to facilities)
Pairing in time of
Generates

## Slide 12: Optical Path
Describes all components through which light passes (fiber + other components)
Can span more than one wellbore
Provides mapping from path length to position in a facility (wellbore or pipeline)
Records defects that impact measurements
Conveyance
Shows changes versus time

## Slide 13: Optical Path Components

## Slide 14: Optical Path Can Span Multiple Facilities

## Slide 15: Fiber may be linear or “folded” along the facility (well, pipeline etc.) being measured

## Slide 16: Optical Path Connectivity Representation
fiber segment 1
connector 1
fiber segment 2
PRODML Network Representation
Network (represents the whole optical path)
Unit (represents each component)
Port (place where component connects)
Node (virtual point of connection)
Port 1
Port 2
Port 1
Port 2
Port 1
Port 2
Node a
Node b
Node…
Ins. Box port
First component (and terminator*) can name Instrument Box port connected
Each unit has 2 ports
Ports with a common “connected Node” are connected
Etc.
Section illustrated
Each component is a “unit”
* - for double ended systems looped back to box

## Slide 17: Fiber Facility Mapping links path distance to facility length, enabling facility “logs” to be made

## Slide 18: Fiber Defects recorded along Optical Path (Example data from OTDR test)

## Slide 19: Optical Path may record changes over time: use of Inventory and Network allows for this

## Slide 20: Simple Optical Path Example

## Slide 21: Optical Path example network showing connectivity

## Slide 22: Instrument Box has properties and records calibration
Properties including reference temperatures, warm up time, etc.
Manufacturer details
Factory calibration details

## Slide 23: Installed System is a combination of Instrument Box + Optical Path
“Single Channel Instrument Box”
One fiber, one box, one facility
= 1 Installed System
“Multiplexed Instrument Box”
One box with multiplex, two facility, two fiber,
= 2 Installed System
Permanent Type
Instrument
Box
Instrument
Box
Well A
Well B

## Slide 24: Installed System (cont.)
“Drive-by” DTS
One box taken to different facility/pre-installed fiber and hooked up for single survey
= 1 Installed System for each “drive-by hook up”
“Logging Operation”
One temporary fiber, one box, one facility
= 1 Installed System for each “logging operation”
Temporary Type
Instrument
Box
Instrument
Box
Instrument
Box
Instrument
Box
Well A
Well B
Well C

## Slide 25: DTS Measurement is the output from an operational DTS & is divided into two parts
The measured trace set which:
  Is indexed against fiber distance
  Can contain a controlled list of curves corresponding to “raw” data and temperature
The interpretation log set which:
  Is indexed against facility length for a specific facility (e.g., like a well log)
  Can contain only the processed temperature result

## Slide 26: DTS Measurement Concept: 1 – record measured trace; 2 – record interpreted log

## Slide 27: DTS Measurement – contains:
Only one set of traces/logs for a single DTS acquisition (over a time range)
Can contain “child” logs/traces which have been processed from parent logs, e.g. by averaging (parents may be in multiple other logs), recalibrated (from a parent), etc.
Measurement Tags to ID events, e.g. well start up; Diagnostic Parameters

## Slide 28: Multiple DTS interpretation logs in one transfer, showing preferred log, parentage, and processing type

## Slide 29: Facility Mapping could be used to define “zones”, e.g. contact intervals, to be reported using “mini-logs”

## Slide 30: Summary
Major step in DTS reporting upgrades original standard for up to date practices
  Multiple facilities on one path
  Logging and other conveyance
Controlled lists of curves eliminates previous log curve ID ambiguity
Keeps measured and interpreted data together
Supports equipment tracking over time

## Slide 31: Appendix - Technical

## Slide 32: Principle of DTS: Laser light down optical fiber

## Slide 33: DTS uses back-scattered light to measure temperature all along the fiber

## Slide 34: Temperature sampled at regular intervals creating a trace indexed along the fiber